## Slide 1: VPR Assessment of a Novel Partitioning Algorithm
David Munro
Supervised by Oliver Diessel

## Slide 2: Overview
Why and What?
How?
Results.
Limitations.

## Slide 3: Why?
FPGAs are awesome…but more vulnerable to errors caused by e.g. ionising radiation than ASICs.
TMR with partial reconfiguration provides redundancy and error correction.
Make three copies of a circuit, and feed the outputs to a voter.
Once an error is detected we can fix it by selectively reconfiguring the incorrect module.
Need to detect, reconfigure and resynchronise within error rate.
TMR Module 1
Dout1
TMR Module 2
Din
Dout2
TMR Module 3
Dout3
Voter
Dout
Source Cetin & Diessel (2012)
Bad
TMR Module 3
Notes: c.f. scrubbing. Reconfigure entire circuit.
Tradeoffs larger/smaller partitions

## Slide 4: Toolchain
Synthesise
Optimise and Technology Map
TMR
Pack
Place
Route
Partition
Triplicate
Join
Flatten
[Test]
Triplicate and Join treat input as black box, create ‘glue’ from template to wire appropriate bits together in a hierarchical netlist.
Flatten turns netlist back into format for VPR.
Test verifies generated circuit is equivalent to the original.
Notes: Partition, Triplicate and Join written myself, Flatten and Test use ABC.

## Slide 5: How? Partition
Start at output, traverse circuit depth first.
Insert each element into partition.
If inserting the element creates a cycle in that partition, cut it.
If it would exceed recovery time, write the partition out to file, create a new empty partition, and insert into that one instead.
In1
Out1
SpecialIn1
SpecialOut1
In2
Notes: Tried breadth first traversal. Much slower. End up cutting lots of edges -> almost voter per circuit element. Average 100% vs 60% slowdown for small partitions.

## Slide 6: Recovery Time
Reconfiguration Time dominates
Target Virtex 5:
  160 LUT/Latches per reconfiguration area
  36 frames/reconfiguration area
  410ns per frame (@100MHz)
Assumptions:
ClockPeriod ~ 10ns
PipelineSteps ~ 1-10
50 clock cyles/hop
NumPartitions ~ 10
LUTs ~ 1600
Latches ~ 1600

## Slide 7: Results
Using 20 largest MCNC circuits as provided by VTR to benchmark.
Sanity check, all the numbers add up.
Notes: Note – unbalanced. Large differences in chain length, number of outputs. Less than optimal.

## Slide 8: Results
Latency is interesting i.e. hard to predict. Very circuit dependent.
Placer uses simulated annealing, so random factor. Need multiple runs
Chart: Number of Partitions
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 5 | 10
 | 1.2286 | 1.1205 | 1.1528 | 1.2367 | 1.2908 | 1.1929 | 1.2901 | 1.2744 | 1.2646 | 1.2472 | 1.4187 | 1.5281
apex2 | 1.0681 | 1.1045 | 1.1304 | 1.0313 | 1.0012 | 1.0683 | 1.1319 | 1.1365 | 1.2595 | 1.4726 | 1.3603 | 1.6746
/home/dsmu186/ths/workflow/blifs/apex4blif | 1.1698 | 1.1595 | 1.1253 | 1.122 | 1.1248 | 1.1602 | 1.1247 | 1.164 | 1.2816 | 1.2852 | 1.5597 | 1.5231
/home/dsmu186/ths/workflow/blifs/bigkeyblif | 1.0026 | 1.0418 | 1.0183 | 1.0444 | 1.0392 | 1.1799 | 1.0483 | 1.0209 | 1.2735 | 1.4789 | 1.7792 | 1.7118
/home/dsmu186/ths/workflow/blifs/clmablif | 1.0711 | 1.0754 | 1.0664 | 1.0807 | 1.0875 | 1.0471 | 1.1327 | 1.1778 | 1.7618 | 1.6635 | 1.796 | 1.891
/home/dsmu186/ths/workflow/blifs/desblif | 1.1594 | 1.1614 | 1.1587 | 1.0799 | 1.0747 | 1.1603 | 1.0777 | 0.99759 | 1.3246 | 1.4503 | 1.3626 | 1.6481
/home/dsmu186/ths/workflow/blifs/diffeqblif | 1.0344 | 1.0176 | 1.0344 | 1.0341 | 1.0338 | 1.0341 | 1.0341 | 1.0176 | 1.0537 | 1.5404 | 1.4769 | 1.651
/home/dsmu186/ths/workflow/blifs/dsipblif | 1.081 | 1.1193 | 1.1968 | 1.1716 | 1.17 | 1.1507 | 1.1402 | 1.2522 | 1.899 | 1.8797 | 1.6029 | 1.7244
/home/dsmu186/ths/workflow/blifs/ellipticblif | 1.1046 | 1.1102 | 1.1241 | 1.1082 | 1.0934 | 1.125 | 1.1231 | 1.2075 | 1.5194 | 1.505 | 1.6721 | 2.1807
/home/dsmu186/ths/workflow/blifs/ex1010blif | 1.1394 | 1.1317 | 1.105 | 1.2164 | 1.1409 | 1.1386 | 1.1058 | 1.2456 | 1.269 | 1.5816 | 1.5005 | 1.4972
/home/dsmu186/ths/workflow/blifs/ex5pblif | 1.073 | 1.241 | 1.1185 | 1.2795 | 1.2771 | 1.1169 | 1.3211 | 1.2345 | 1.2821 | 1.2306 | 1.4598 | 1.724
Chart: Average slowdown vs partitions
| 1 | 1 | 1 | 1 | 1 | 1 | 1.1499999999999999 | 1.6 | 3.5 | 6.65 | 9.75 | 37.8125
 | 1.1682 | 1.1485 | 1.1574 | 1.1534 | 1.1518 | 1.1488 | 1.1741 | 1.1919 | 1.3861 | 1.4869 | 1.5773 | 1.7125

## Slide 9: Results
Notes: Need to average across more runs still

## Slide 10: Limitations
Implementation to evaluate effectiveness, missing some functionality e.g.
  Can’t constrain placement to ensure partitions are actually mapped to separate reconfiguration areas.
  Our target architecture is still a theoretical simplified version. Only latches and LUTs.
  Using a simplified voter (only one 3-LUT).
Partitioner is still an early version. Many optimisations to be made.