## Slide 1: VPR Assessment of a Novel Partitioning Algorithm
David Munro
Supervised by Oliver Diessel

## Slide 2: Overview
Why and What? Quick discussion of motivation, and what this thesis is actually doing.
How? Very high level look at the implementation.
Results. The interesting bit.
Limitations. Every project has them.

## Slide 3: Why?
FPGAs are awesome…but vulnerable to configuration errors caused by e.g. space radiation, that ASICs aren’t.
TMR with partial reconfiguration provides redundancy and error correction.
Make three copies of a circuit, and feed the outputs to a voter.
Once an error is detected we can fix it by selectively reconfiguring the incorrect module.
Need to detect, reconfigure and resynchronise within error rate.
TMR Module 1
Dout1
TMR Module 2
Din
Dout2
TMR Module 3
Dout3
Voter
Dout
Source Cetin & Diessel (2012)
Bad
TMR Module 3
Notes: Triple Modular Redundancy (TMR) is a popular approach to mitigating the effects of SEUs
  The user design is triplicated and the outputs from each module are fed into a voting circuit to determine the correct output value
TMR significantly improves system reliability and availability in the presence of SEUs
However, TMR results in substantial overhead in terms of area and power consumption.
  selective/partial TMR and voter insertion has been used to minimize the overheads associated with TMR, in terms of area, clock speed and power consumption
  Comes at the cost of reduced system reliability and availability, which may be undesirable for some applications

## Slide 4: Why
TMR entire circuit -> lower overhead, lower fault tolerance (higher recovery time).
TMR every component in circuit -> higher fault tolerance, higher overhead (4x instead of 3x).
Middle ground, TMR sections such that we meet target fault tolerance.
What is a reasonable Error Recovery Time? User specified, depends on application. For space based applications 1.4s mean time between errors1.
1. P. J. Pingree, “Advancing NASA’s on-board processing capabilities with reconﬁgurable fpga technologies”. Aerospace Technologies Advancements.

## Slide 5: Toolchain
Synthesise
Optimise and Technology Map
TMR
Pack
Place
Route
Partition
Triplicate
Join
Flatten
[Test]
Insert new ‘TMR’ step in normal CAD toolchain.
TMR consists of several substeps, each a separate module.
Triplicate and Join treat input as black box, create ‘glue’ from template to wire appropriate bits together in a hierarchical netlist.
Partition is more complicated.
Flatten turns netlist back into format for VPR.
Test verifies generated circuit is equivalent to the original.

## Slide 6: How? - Partition
Start at output, traverse circuit depth first.
Visit each element once and only once. As you do, insert it into current partition.
If inserting the element creates a cycle, cut it.
If it would exceed recovery time, write the partition out to file, create a new empty partition, and insert into that one instead.
Repeat until entire circuit is partitioned.
In1
Out1
SpecialIn1
SpecialOut1
In2

## Slide 7: Recovery Time
Recovery time is error detection time + communication delay + reconfiguration time + resynchronisation time.
Reconfiguration Time dominates

## Slide 8: Results
Some results use old formula for RecoveryTime -> Number of partitions and RecoveryTime may be different in final results. Overall trends and results still hold. No major changes.
Area usage is 3x + a bit. Unsurprising, but a nice sanity check.
SUM(Outputs)=645. NumLUTsTMR =3*Base+645
LatchesTMR=3xBase

## Slide 9: Results
Latency is interesting i.e. hard to predict. Very circuit dependent.
In general, the more partitions, the slower.
Chart: Number of Partitions
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 5 | 10
 | 1.2286 | 1.1205 | 1.1528 | 1.2367 | 1.2908 | 1.1929 | 1.2901 | 1.2744 | 1.2646 | 1.2472 | 1.4187 | 1.5281
apex2 | 1.0681 | 1.1045 | 1.1304 | 1.0313 | 1.0012 | 1.0683 | 1.1319 | 1.1365 | 1.2595 | 1.4726 | 1.3603 | 1.6746
/home/dsmu186/ths/workflow/blifs/apex4blif | 1.1698 | 1.1595 | 1.1253 | 1.122 | 1.1248 | 1.1602 | 1.1247 | 1.164 | 1.2816 | 1.2852 | 1.5597 | 1.5231
/home/dsmu186/ths/workflow/blifs/bigkeyblif | 1.0026 | 1.0418 | 1.0183 | 1.0444 | 1.0392 | 1.1799 | 1.0483 | 1.0209 | 1.2735 | 1.4789 | 1.7792 | 1.7118
/home/dsmu186/ths/workflow/blifs/clmablif | 1.0711 | 1.0754 | 1.0664 | 1.0807 | 1.0875 | 1.0471 | 1.1327 | 1.1778 | 1.7618 | 1.6635 | 1.796 | 1.891
/home/dsmu186/ths/workflow/blifs/desblif | 1.1594 | 1.1614 | 1.1587 | 1.0799 | 1.0747 | 1.1603 | 1.0777 | 0.99759 | 1.3246 | 1.4503 | 1.3626 | 1.6481
/home/dsmu186/ths/workflow/blifs/diffeqblif | 1.0344 | 1.0176 | 1.0344 | 1.0341 | 1.0338 | 1.0341 | 1.0341 | 1.0176 | 1.0537 | 1.5404 | 1.4769 | 1.651
/home/dsmu186/ths/workflow/blifs/dsipblif | 1.081 | 1.1193 | 1.1968 | 1.1716 | 1.17 | 1.1507 | 1.1402 | 1.2522 | 1.899 | 1.8797 | 1.6029 | 1.7244
/home/dsmu186/ths/workflow/blifs/ellipticblif | 1.1046 | 1.1102 | 1.1241 | 1.1082 | 1.0934 | 1.125 | 1.1231 | 1.2075 | 1.5194 | 1.505 | 1.6721 | 2.1807
/home/dsmu186/ths/workflow/blifs/ex1010blif | 1.1394 | 1.1317 | 1.105 | 1.2164 | 1.1409 | 1.1386 | 1.1058 | 1.2456 | 1.269 | 1.5816 | 1.5005 | 1.4972
/home/dsmu186/ths/workflow/blifs/ex5pblif | 1.073 | 1.241 | 1.1185 | 1.2795 | 1.2771 | 1.1169 | 1.3211 | 1.2345 | 1.2821 | 1.2306 | 1.4598 | 1.724
Chart: Average slowdown vs partitions
| 1 | 1 | 1 | 1 | 1 | 1 | 1.1499999999999999 | 1.6 | 3.5 | 6.65 | 9.75 | 37.8125
 | 1.1682 | 1.1485 | 1.1574 | 1.1534 | 1.1518 | 1.1488 | 1.1741 | 1.1919 | 1.3861 | 1.4869 | 1.5773 | 1.7125

## Slide 10: Results

## Slide 11: Results
Placer uses simulated annealing -> Random factor.
Generally runs are within 10-20%, but some outliers.
Need to take average across multiple runs (aiming for 10 runs).

## Slide 12: Results
We traverse circuit to add nodes depth first i.e. explore children before finishing current level.
Significantly better results than breadth first. Far fewer voters and wires between partitions, so less slowdown.

## Slide 13: Limitations
Implementation to evaluate effectiveness, missing some functionality.
E.g. Can’t constrain placement to ensure partitions are actually mapped to separate reconfiguration areas.
Our target architecture is still a theoretical simplified version. Only latches and LUTs.
Partitioner doesn’t try very hard to be optimal.