## Slide 1: Partitioning Algorithm and Initial Results

## Slide 2: Workflow
Synthesis
Optimisation
Partitioning
  Split
  Triplicate
  Join
  Flatten
Packing
Placing
Routing
CAD Design Flow (VPR Manual)

## Slide 3: Blif Format
Text format.
List of elements/nodes. Latches and Combinational Logic.
Each node has text describing inputs, outputs, element.
E.g (And Gate):
.names in1 in2 out
11 1

## Slide 4: Algorithm
1. Read entire file into memory, and represent it as a graph.
Each Model has a list of nodes and map of signalName->Signal
Each signal points to its source and sinks
Each node has a list (string) of inputs and outputs (+type, etc).
Why do nodes have strings, which are looked up in a map to the signal, which points to the node? Why not have each node just point to the other node? Because of the way models are made and manipulated.

## Slide 5: Algorithm 2
2. Traverse
Start at one end, adding connected nodes to partition. Once partition reaches limit, write it out, remove those nodes from the network, and repeat.
Specifically, start at outputs not inputs due to e.g. [IMAGE]
3. Adding to Partition
Add to node collection
Update Signals
Recalculate critical path (max cost without cycles)

## Slide 6: Algorithm 3
model = network->MainModel
FOREACH output in model
q.Add(output->source)
partition = EmptyModel
WHILE node = q.pop
IF visited(node)
CONTINUE
IF partition+node > limits
WriteModelToNewFile(partition)
partition = EmptyModel
partition.Add(node)
FOREACH input in node->inputs
q.Add(input->source)
WriteModelToNewFile(partition)
Model::Add(node)
nodeCollection.Add(node)
UpdateSignals(node)
inCost = MaxInputCost
UpdateCosts(node, inCost)
Model::UpdateCosts(node, inCost)
nodeCost = inCost+InnateCost
MarkVisited(node)
FOREACH sink in node->sinks
IF visited(sink)
Cut(node, sink)
ELSE
UpdateCosts(sink, nodeCost)
//Rename the signals, then after TMR we can rejoin them outside the partition
Model::Cut(source, sink)
source->output = "SpecialOut"+source->output
sink->inputs[source->output] = "SpecialIn"source->output
Model.AddInput("SpecialIn"source->output)
Model.AddOutput("SpecialOut"+source->output)

## Slide 7: Results
Use very small partitions, to magnify effect.
Routing is still the dominant contributor to time spent in workflow.
Latency from 10%-80% increase.
Area, number of elements, etc, all more or less triple.
Number of nets on the critical path usually increases, sometimes decreases.